## Slide 1: Introduction to Six Sigma
Prepared By:
Said Fawzy
Manager of Information Center –Quality manager
Tendering Department
Arab Contractors
المعهد التكنولوجى لهندسة التشييد و الإدارة

## Slide 2
Chapter 03 :

## Slide 11
Chapter 04 :

## Slide 41
Questions

## Slide 42
Question 1
For a 4 step process with yield = (1-p) = 90% at each step, what is the overall Process Yield?
90%
72.9%
65.61%
59.05%
Explanation
The Process Yield is calculated through (1-p)^n where (1-p) is 90% and n is 4.
Process Yield = (90%)^4 = 65.61%

## Slide 43
Question 2
Given a production process with three production steps as shown above, what is the overall Process Yield if the first production step has a yield of 98%; the second, of 99%; and the third, of 85%?
94.1%
94.7%
81.9%
82.5%
Explanation
If the production consists of three steps that each have a different Process Yield, then the overall Process Yield is calculated by: 0.98×0.99×0.85=0.82467 (≈82.47%)

## Slide 44
Question 3
For 2 process steps, each with 5% fraction defective, what is our final Process Yield?
0.25%
90.25%
97.5%
85.74%
Explanation
Since 5% of the production at each step is defective, p = 0.05 and the number of steps is n=2.
Process Yield = (1-p)^n = (1-0.05)^2 = (0.95)^2 = 90.25%

## Slide 45
Question 4
For 4 process steps, each with a yield of 25%, what is our final Process Yield?
31.64%
0.39%
30%
1.73%
Explanation
Since the yield at each step is 25% of the production at each step, (1-p) = 0.25. The number of steps is n=4.
Process Yield = (1-p)^n = (0.25)^4 = 0.00396 = 0.3906% (≈0.39%)

## Slide 46
Question 5
For a 95% yield at each step what is the ppm (Parts per Million) defective?
95000
50000
950000
500000
Explanation
p = 1-0.95 = 0.05
ppm = 0.05x1000000 = 50000

## Slide 47
Question 6
For a 99.999% yield at each step what is the ppm (Parts per Million) defective?
1000
100
1
10
Explanation
p = 1-0.99999 = 0.00001
ppm = 0.00001x1000000 = 10

## Slide 48
Question 7
What is the difference between Defects and Defectives?
A defect occurs when an item is unacceptable. A defective process occurs when the process outcome is not the expected outcome.
A defect occurs when the process outcome is exactly the expected outcome. A defective item is unacceptable due to one or more defects.
A defective occurs when a process outcome is not the expected outcome. A defect item is unacceptable due to one or more defects.
A defect occurs when a process outcome is not the expected outcome. A defective item is unacceptable due to one or more defects.
Explanation
See Lecture

## Slide 49
Question 8
Which are the correct definitions of Defects per Unit (DPU) and Defects per Million Opportunities (DPMO)?
DPU = (Total # of Defectives)/(Total # of Units); DPMO = (DPUx1000000)/(Total # of Units)
DPU = (Total # of Defects)/(Total # of Units); DPMO = (DPUx1000000)/(Total Opportunities for a Defect in One Unit)
DPU = (Total # of Units)/(Total # of Defects); DPMO = (DPUx1000000)/(Total Opportunities for a Defect in One Unit)
DPU = (Total # of Defects)/(Total # of Units); DPMO = (DPUx1000000)/(Total # of Units)
Explanation
See Lecture